# Serial protocol

Protocol work on a client server mode.
The server is the speed controler, it responds to client requests on the serial line.

The protocol allows to read or write a series of variable in the memory of the speed controler.

Each variable is represented as a 16 nits signed interger. The meaning and interpretation of each variable is given in a table bellow.

## Message description
### Read variable request message:
Header	Message Type	Variable address	Checksum
0x53 ('S')	0x52 ('R', Read)	0xnn	0xcc

### Read variable response message:
Header	Message Type	Variable address	MSB	LSB	Checksum
0x53 ('S')	0x52 ('R', Read)	0xnn	0xmm	0xll	0xcc

### Write variable request message:
Header	Message Type	Variable address	MSB	LSB	Checksum
0x53 ('S')	0x57 ('W', Write)	0xnn	0xmm	0xll	0xcc

### Write variable reponse message:
Header1	Message Type	Variable address	Checksum
0x53 ('S')	0x52 ('W', Write)	0xnn	0xcc

### Error reponse message:
Header	Message Type	Variable address	Error indicator	Checksum
0x53 ('S')	0x55 ('E', Error)	0xnn	0x01 : address out of bound / 0x02 : not writable	0xcc

## Serial parameters

Serial line shall be configured with the following parameters
- 8 bits
- 9600 bauds
- 1 bit stop

# Variables list

Name	Access	Address	Value
Input speed frequency	Read only	0x00	0,01Hz
Output speed frequency	Read only	0x01	0,01Hz
Input ref pt1	Read/write	0x03	0,01Hz
Output1 ref pt1	Read/write	0x04	0,01Hz
Input ref pt2	Read/write	0x05	0,01Hz
Output1 ref pt2	Read/write	0x06	0,01Hz
Input ref pt3	Read/write	0x07	0,01Hz
Output2 ref pt2	Read/write	0x08	0,01Hz
Output2 ref pt2	Read/write	0x09	0,01Hz
Output2 ref pt3	Read/write	0x0a	0,01Hz